## Slide 1
Memory Hierarchy
Cache Memories
Program Optimization
MADE BY: Sun Shaocong & Shi Zhuming
THANKS TO: Zhong Zhineng & Song Yixin

## Slide 2
Memory Hierarchy

## Slide 3
Example

## Slide 4
RAM: SRAM & DRAM
Disk
Bus structure
Storage Technology

## Slide 5
Random Access Memory (RAM)
  Volatile, expensive, compared to hard disk
SRAM versus DRAM
  SRAM doesn’t need refresh
    faster and stable, more expensive
    used as cache memories
  DRAM
    higher density, lower power consumption
    used as main memory
RAM

## Slide 6
Row Access Strobe (RAS)
Column Access Strobe (CAS)
Memory module: Read & Write a word
FPM DRAM, SDRAM, DDR SDRAM
DRAM: Access

## Slide 7
nonvolatile, compared to RAM
PROM: only programmed once
EPROM
EEPROM -> flash memory
firmware: stored in ROM
ROM

## Slide 8
Bus transaction: read and write
System bus: connecting CPU and I/O bridge
Memory bus: connecting I/O bridge and main memory
I/O bus: disk, graphic card and other buses
BUS

## Slide 9
Capacity:
Access time:
  avg seek time + avg rotation time + avg transfer time
DISK

## Slide 10
K(kilo), M(mega), G(giga), T(tera): context dependent
DRAM & SRAM: , , ,
Disk & network: , , ,
Unit Conversion

## Slide 11
Solid State Disk (SSD)
Sequential access faster than random access
Write slower than Read
Modifying a block page requires full page erasure and copy
SSD

## Slide 12
Developing Tendency

## Slide 13
Temporal locality
Spatial locality
Data-access: temporal locality or spatial locality:
  The smaller the step length, the better the spatial locality.
  Repeating references to the same variable has the temporal locality.
Instruction-fetch: both locality:
  The smaller the loop body and the more the number of iteration, the better the locality.
Locality

## Slide 14
Cache Memories

## Slide 15
Small and fast SRAM memories
Keep frequently accessed blocks of main memory
Cache hit
Cache miss: three types of miss
Cache Memories

## Slide 17
Cache Structure
M, S, E, B, m, s
S cache sets, E cache lines, B blocks
t = m-(b+s) tag bits
Valid bit
C = S×E×B
Address of word: tag + set index + block offset
Bijection from middle s set index bits to S cache sets
Bijection from low b block offset bits to B blocks
2^t address of a cache set => t tag bits

## Slide 18
Cache Structure

## Slide 19
Direct Mapped Cache (E = 1)
  Not match: old line being replaced directly
  Thrash
Associative Cache (1 <E < C/B)
  Not match: one line in the set is selected for eviction and replacement
  Many replacement policies: Random, LRU, LFU, …
Fully Associative Cache (S = 1, E = C/B)
  Search for many matching tags in parallel => expensive and small
  TLB
Cache Classification

## Slide 20
Write hit
  Write-through
  Write-back
Write miss
  Write allocate
  No write allocate
Write through + No write allocate / Write back + Write allocate
Cache Write

## Slide 21
Make use of locality
Make the most frequent the fast
Decrease cache miss within loops
Loop variable orders
Cache Friendly Code

## Slide 22
Cache Mountain

## Slide 23
Program Optimization

## Slide 24
Compiler Optimization
Some can be done by compiler
  Code moving, such as moving the repeating calc inside the loop outside.
  Use shift and add/sub to do mult/div
  Expression reuse
Some cannot be done by compiler (must be conservative)
  Procedure may have side-effects
  Pointer may have aliases

## Slide 25
CPI may be less than 1
In-order issue
Out-of-order execution
In-order commit
Simple Out-of-order Processor

## Slide 26
Out-of-order execution
Multiple issue
Dynamic Scheduling
Speculative execution
Register renaming
Modern CPU

## Slide 27
Critical Path
Critical path: lower bound
Number of function parts
Data passing limitation

## Slide 28
Loop Unrolling: Improve Parallelism

## Slide 29
Separate Accumulators

## Slide 30
Reassociation

## Slide 31
Limitations
Register spilling: k = 20, use stack to store
Floating operation does not have associative law, so changing operation orders may not apply.